## Slide 1: IT1020 – Introduction to computer systems
Lecture 6: combinational and sequential Logic circuits

## Slide 2: Lecture content
Combinational circuits
Sequential circuits
Difference between combinational and sequential circuits
Types of combinational and sequential circuits

## Slide 3: Digital Logic Circuits
Logic circuits can be categorized as
Combinational Circuits
Sequential circuits.
A combinational circuit consists of input variables, logic gates and output variables.
  Output depends only on current input
  Has no memory
LECTURE 04 - LOGIC & CONTROL - PART I

## Slide 4: Combinational circuits
A combinational circuit consists of input variables, logic gates, and output variables.
5

## Slide 5: Combinational Circuits (Examples)
6

## Slide 6: Sequential Logic
Sequential Logic:
Output depends not only on current input but also on past input values, e.g., design a counter
Need some type of memory to remember the past input values
2019/3/15
SEQUENTIAL CIRCUITS
PJF - 7

## Slide 7: Combinational vs. Sequential Circuits
n-inputs
m-outputs
Combinational Circuit
Storage Elements
Next
state
Present
state
Sequential Circuit
n-inputs
Combinational Circuit
m-outputs
(Depend only on inputs)
Combinational Circuit

## Slide 8: Combinational Circuits - Half Adder
Half Adder : The sum is XOR operation and the carry an AND
Sum= A’B+AB’
A + B
Carry=AB
Truth table for 1 bit addition and a circuit for a half adder

## Slide 9: Combinational Circuits – Full Adder
Input |  |  | Output | 
x | y | z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 10: Binary Multiplication
12

## Slide 11: Shifter
Right shift 1-bit
Left shift 1-bit

## Slide 12: Shifter
Figure shows an eight-input, eight- output, 1-bit left/right shifter.
An eight-bit input is applied onto D0, D1…D7, and the shifted output is taken out of S0, S1…S7.
The shift direction is controlled with the control signal C.
A logic one on C enables the right hand side AND gates and pass each input bit to the OR gate to its right and hence, a one-bit right shift is performed.
Similarly, a logic zero on C performs a left shift.
A 1-bit left/right shifter.

## Slide 13: Comparator
A comparator circuit compares two input words.
The simplest comparator circuit is an exclusive NOR gate, which compares two individual bits:
produces a zero if the two bits are unequal
produces a logic one if they are equal

## Slide 14: Comparator
When two words of length n are to be compared,
n XOR gates and
a NOR gate can be combined
A 4-bit comparator

## Slide 15: Decoder/Encoder
Decoder
A combinational circuit that converts binary information from the
n coded inputs to a maximum of 2n unique outputs
n-to-m line decoder = n x m decoder Ex: Octal to Binary line decoder
  n inputs, m outputs (3 inputs, 8 outputs)
If the n-bit coded information has unused bit combinations, the decoder may have less than 2n outputs
  m  2n

## Slide 16: Binary Decoder
Black box with n input lines and 2n output lines
Binary
Decoder
n inputs
2n outputs

## Slide 17: 2-to-4 Binary Decoders
From truth table, circuit for 2x4 decoder is:
Note: Each output is a 2-variable minterm
(X'Y', X'Y, XY' or XY)
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 0 |  | 0 | 0 | 1
F0 = X'Y'
F1 = X'Y
F2 = XY'
F3 = XY
X
Y
Truth Table:
X
Y
F0 F1 F2 F3
2-to-4 Decoder
E

## Slide 18: 2-to-4 Decoders : NAND Implementation
LECTURE 06 - LOGIC & CONTROL - PART III
Decoder is enabled when E=0 and an output is active if it is 0

## Slide 19: 3-to-8 Binary Decoder
x | y | z | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  |  | 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 1 |  |  |  |  |  |  | 
x
y z
F = x'y'z'
0
F1 = x'y'z
F2 = x'yz' F3 = x'yz F4 = xy'z' F5 = xy'z
6
F = xyz'
7
F = xyz
Truth Table:
X
3-to-8
Decoder
F0 F1
F2
F3 F4 F5 F6 F7
Y
Z

## Slide 20: Decoder Expansion
Decoder expansion
Combine two or more small decoders with enable inputs to form a larger decoder
3-to-8-line decoder constructed from two 2-to-4-line decoders
  The MSB is connected to the enable inputs
  if A2=0, upper is enabled; if A2=1, lower is enabled.

## Slide 21: Decoder Expansion(Contd.)

## Slide 22: Combining two 2-4 decoders to form one 3-8 decoder using enable switch
The highest bit is used for the enables

## Slide 23: Combinational Circuit Design with Decoders
Combinational circuit implementation with decoders
A decoder provide 2n minterms of n input variables
Since any Boolean function can be expressed as a sum of minterms, one can use a decoder and external OR gates to implement any combinational function.

## Slide 24: Combinational Circuit Design with Decoders
Example Realize F (X,Y,Z) = Σ (1, 4, 7) with a decoder:

## Slide 25: Encoder
Inverse Operation of a decoder 2n input, n output
3 OR Gates Implementation
A0 = D1 + D3 + D5 + D7
A1 = D2 + D3 + D6 + D7
A2 = D4 + D5 + D6 + D7
Inputs |  |  |  |  |  |  |  | Outputs |  | 
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | A2 | A1 | A0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
Truth Table for Encoder

## Slide 26: Multiplexer (MUX)
A combinational circuit that receives binary information from one of 2n input data lines and directs it to a single output line
A 2n -to 1 multiplexer has 2n input data lines and n input selection lines
lines and n input selection lines
4-to-1 multiplexer Diagram
4-to-1 multiplexer Function Table
Select |  | Output
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
I0
I1
I2
I3
S0 S1
Y
Function Table for 4-to-1 line Multiplexer
4-to-1 Line Multiplexer
Usage: Data routing, Parallel-to-serial conversion, Operation sequencing, Implement logic function of a truth table

## Slide 27: Basic 2-Input Multiplexer
S | OUTPUT
0 | Z=I0
1 | Z=I1
INPUTS
I1
DA TA
I0
S
SELECT INPUT
Z  I0  S  I1  S

## Slide 28: 4-Input Multiplexer
I0
I1 I2 I3
S1 | S0 | OUTPUT
0 | 0 | Z=I0
0 | 1 | Z=I1
1 | 0 | Z=I2
1 | 1 | Z=I3
S1 S0
Select Inputs

## Slide 29: Multiplexer Logic Diagram
I
I1 I2
0
I3
I4 I5
6
I I
7
E S
2
1
S S
0
74151
MUX
D A T A
I N P U T S
SELECT LINES
Z
_
Z
Takes one of many inputs and funnels it to an output Z.
Take the selector lines convert to a decimal number and this is the input funneled to the output.
Strobe is active low enable
S2 | S1 | S0 | E | Z
0 | 0 | 0 | 0 | I0
0 | 0 | 1 | 0 | I1
0 | 1 | 0 | 0 | I2
0 | 1 | 1 | 0 | I3
1 | 0 | 0 | 0 | I4
1 | 0 | 1 | 0 | I5
1 | 1 | 0 | 0 | I6
1 | 1 | 1 | 0 | I7

## Slide 30: Multiplexer
8-line to 1-line multiplexer

## Slide 31: Programmable Logic Arrays (PLA)
Programmable logic arrays (PLA) are very general chips that provide a quick and easy way to implement Boolean functions expressed in the sum-of-products form.
A PLA comprises of an array of AND gates and another array of OR gates.
  Each one of the AND gate outputs is tapped through tiny fuses to the
inputs of each OR gate.
  Similarly, the input lines of the PLA chip are tapped to the inputs of each AND gate.
Applying a high voltage to the chip a designer can blow selected fuses leaving only the desired circuit connections intact.
Therefore, by choosing the proper set of fuses to blow, a designer can
implement or “program” the desired Boolean functions rapidly.

## Slide 32: Programmable Logic Arrays (PLA)

## Slide 33: Arithmetic Logic Unit (ALU)
At the heart of any computer CPU is the arithmetic logic unit or the ALU.
It is a circuit that performs AND, OR, and sum operations of two input words.
AND and OR logical operations are easily implemented
using the corresponding logic gates.
The sum operation is achieved using the full adder circuit described earlier.

## Slide 34: Arithmetic Logic Unit (ALU)

## Slide 35: Arithmetic Logic Unit (ALU)
If the CPU uses n-bit machine words, then n such ALU blocks must be connected together.
While the AND and OR operations only need the n ALUs to be placed in the n bit positions, the SUM operation requires the Carry-in and Carry- out signals of adjacent units cascaded

## Slide 36: Arithmetic Logic Unit (ALU)
Cascading eight 1-bit ALUs to form an 8-bit ALU

## Slide 37: Sequential Circuits
A sequential circuit is an interconnection of flip flops and Gate
Clocked synchronous sequential circuit
Flip-Flop Input Equation
Boolean expression for F/F input
Input Equation
  DA = Ax + Bx, DB = A’x
Output Equation
  y = Ax’ + Bx’
Combinational Circuit = Gate Sequential Circuit = Gate + F/F
Combinational Circuit
Flip-Flops
Input
Output
Clock
Q
SET
Q
CLR
D
Q
SET
Q
CLR
D
x
DA
DB
A
A’
B
B’
Clock
y

## Slide 38: Sequential Circuits
J Q
K Q
SET
CLR
J Q
K Q
SET
CLR
Clock
x A
B
Sequential Circuit Design Procedure
Recall Combinational Circuit Design Sequential Circuit: State diagram, State table F/F : 2m+n (m - State , n - Input )
The Problem is stated
I/O variables are assigned
Truth table(I/O relation)
Simplified Boolean Functio
Logic circuit diagram

## Slide 39: Latches – SR Latch
SR Latch
Characteristic Table

## Slide 40: Latches – D Latch
Latches
D Latch

## Slide 41: Clock Signals
Clock signals are used to maintain the desired timing in the circuits.
Clock circuits emit pulse trains of precise repetition interval and width.
Sometimes it is necessary to have one clock pulse train trail another by a fixed time.
A circuit with the appropriate delay may be inserted to achieve the desired phase shift
(a) Clock circuit, (b) the clock waveforms

## Slide 42: Flip-flops

## Slide 43: Edge-Triggered Flip Flops
State Change : Clock Pulse
  Rising Edge(positive-edge transition)
  Falling Edge(negative-edge transition)
Setup time(20ns)
Minimum time that D input must remain at constant value before the transition.
Hold time(5ns)
  Minimum time that D input must not change after the positive transition.
Propagation delay(max 50ns)
  time between the clock input and the response in Q
ts th
Positive clock transition

## Slide 44: SR Flip-flop
Characteristic Table

## Slide 45: D Flip-flop
Characteristic Table

## Slide 46: Use of Circuits: Memory

## Slide 47
THANK YOU
End of Computer Fundamental Section